## Slide 1: cvV cwiwPwZ
wWwm †gwkbm (66742) ce©t PZz_©, †UK‡bvjwRt B‡jKwUªK¨vj Aa¨vq-(13) jm Ges `ÿZv
Pjgvb....

## Slide 2
wkLbdj
GB cvV †k‡l wkÿv_©xiv..
1| wWwm †gvU‡ii jm wK Ges GKB mv‡_ j‡mi Køvwmwd‡Kkb ej‡Z cvi‡e|
2| wWwm †gvU‡ii cvIqvi †÷R eY©bv Ki‡Z cvi‡e|
3| wWwm ‡gvU‡ii `ÿZv m¤úwK©Z MvwYwZK mgm¨vi mgvavb Ki‡Z cvi‡e|
Pjgvb....

## Slide 3
wWwm †gvU‡ii jm mgyn
wWwm †gvU‡ii Bbcy‡U †h cwigvb ‰e`¨ywZK kw³ mieivn Kiv nq AvDcy‡U †m cwigvY hvwš¿K kw³ cvIqv hvq bv¦ A_©vr †h hvwš¿K kw³ wWwm †gvU‡ii AvDcy‡U cvIqv hvq bv Zv‡K jm e‡j¦
Pjgvb....

## Slide 4
Losses of DC Motor
Core loss
Copper Loss
Hysteresis loss
Mechanical Loss
Eddy Current Loss
Armature winding copper loss
Field winding copper loss
Series field copper loss
Shunt field copper loss
Brush & Bearing friction loss
Air friction loss
†gvU‡ii GB jm¸‡jv‡K wb¤œwjwLZ fv‡M fvM Kiv hvq
Pjgvb....

## Slide 5
Power Stage of DC Motor:
Electrical I/P
Or
Motor I/P
= V×IL (W)
Armature G mechanical Power developed
= Eb×Ia (W)
Motor O/P
= B.H.P
= B.H.P×735.5 (W)
Copper
Loss
Iron & Friction Loss
A
C
B
Dc‡ii QK †_‡K wWwm ‡gvU‡ii wZb cÖKvi `ÿZv cvIqv hvq¦ 1. Overall efficiency %η= ×100 2. Mechanical efficiency %η= ×100 3. Electrical efficiency %η= ×100
Pjgvb....

## Slide 6
Formula 1. No Load Input = VIaNL 2. Full Load Armature Current (IaFL) = IFL-Ish 3. No Load Armature Cu Loss (PcuNL) =I2aNL ×Ra 4. Full Load Armature Cu Loss(PcuFL) =I2aFL×Ra 5. Back e.m.f (Eb) =V – IaRa 6. Generator b¨vq Motor Gi Back e.m.f (Eb) = 7. Output = Input-Total Loss 8. Total Loss = Armature Cu Loss + Constant Loss 9. Kg©`ÿZv = x 100 10. Torque, Ta= 9.55
Pjgvb....

## Slide 7
wWwm ‡gvU‡ii `ÿZv m¤úwK©Z MvwYwZK mgm¨v¦
Pjgvb....

## Slide 8
P-(1) 220V DC Shunt Machine Gi Armature resistance 0.5Ω, Full Load armature current 20A. Induced e.m.f KZ? 1) Generator n‡j 2) Motor n‡j ¦
Soln : When Generator:- Eg = V + IaRa = 220 + (20×0.5) = 230 V (Ans:-) When Motor:- Eb= V - IaRa = 220 - (20×0.5) =210V(Ans:-) | Given, V= 440 V Ra= 0.5Ω Ia= 20A Eg= ? Eb= ?
Pjgvb....

## Slide 9
P-(2) GKwU 440 V Shunt Motor Gi Armature resistance 0.8Ω field resistance 200Ω find back e.m.f when output 7460 W at 85% efficiency.
Soln : Motor I/P = = = 8776.47W IL= = 19.94 A Ish= = 2.2 A Ia=19.94 -2.2 = 17.74 A Eb= V –IaRa= 440-(17.74 × 0.8) = 425.8 V (Ans) | Given, Pout = 7460W Ra= 0.8Ω Rsh= 200Ω = 85% V= 440 V Eb= ?
Pjgvb....
Ra

## Slide 10
P-(3) GKwU DC Motor 110A & 480V Armature resistance 0.2Ω machines pole 6 lap connected, conductor number 864, flux 0.05wb. Find out 1) speed 2) gross torque developed.
Soln : We Know, Eb= V – IaRa = 480-(110 X 0.2) = 458V Now, Eb= Or, 458 = N= 636 r.p.m (Ans:-) Again, Ta= 9.55 = 9.55 × = 756.5 N-m (Ans:-) | Given, Ia = 110A Ra= 0.2Ω Z= 864 P= 6= A V= 480 V N = ? Ta= ?

## Slide 11
Pjgvb....
P-(4) GKwU js kv›U K¤úvD›U ‡gvUi 220V mieivn n‡Z 20A Kv‡i›U †bq¦ Av‡g©Pvi, wmwiR Ges kv›U wdì ‡iva 0.25Ω, 0.45Ω Ges 55Ω¦ hw` Avqib, wd«Kkb Ges DB‡Ûm jm¸‡jv GK‡Î 600W nq, Z‡e ‡gvU‡ii `ÿZv wbY©q Ki ¦
Ish
Soln :
Rsh
Rse
Ra
Ia
IL
V

## Slide 12
We Know, Ish = = 4A IaIL-Ish= 20-4 =16A Shunt Field Copper Loss = I2shRsh = (4)2×55=880W Armature Cu Loss =Ia2× (Ra+Rse) =(16)2× (0.25+0.45) =179.2W Total Loss = Shunt Field Loss + Cu Loss + Iron Loss =(880+179.2+600) = 1659.2W Motor Input=VIL= 220X20 = 4400W Motor Output=Input-Total Loss = (4400-1650.2) = 2740.8W η = 100 = 100 = 62.29% (Ans) | Pjgvb.... Given, V = 220V IL = 20A Ra = 0.25Ω Rse=0.45Ω Rsh = 55Ω pi = 600W η =?
 | Pjgvb.... Given, V = 220V IL = 20A Ra = 0.25Ω Rse=0.45Ω Rsh = 55Ω pi = 600W η =?
V
Ish
Rse
Rsh
IL
Ra
Ia

## Slide 13
P-(5) GKwU 220VGi kv›U ‡gvUi mieivn jvBb n‡Z †jvWk~b¨ Ae¯’vq 5AGes c~Y© †jvWmn Pjvi mgq 80A Kv‡i›U MÖnb K‡i¦ Av‡g©Pvi Ges kv›U wdì ‡iva 0.3Ω Ges 250Ω¦ hw` ‡gvU‡I c~Y© †jvW †`qv nq, Z‡e Gi Kg©`ÿZv Ges Drcvw`Z Ak¦kw³ (HP) wbb©q Ki¦
Soln :
Ra
Pjgvb....
INL
IFL
Ia1
Ia2

## Slide 14
We Know, No Load Input = VIa0 = 230X5 = 1150W Ish = = 0.92A No Load Armature Current(Ia1) = INL- Ish = 5-0.92 = 4.08A No Load Armature Cu Loss(PcuN) = (Ia1) 2 X Ra= (4.08) 2×0.3 = 5W Constant Loss(Pc) = VINL-Pcu=(230×5)-5= 1145W Full Load Input = VIFL= 230×80 = 18400W Full Load Armature Current(Ia2) = IFL- Ish= 80-0.92 = 79.08A Full Load Armature Cu Loss(PFcu) = (Ia2) 2×Ra= (79.08) 2×0.3=1876W Total Loss = Full Load Armature Cu Loss + Constant Loss = 1876+1145 = 3021W Output = Input- Total Loss = 18400-3021= 15379 W Kg©`ÿZv = x 100 = 100 = 83.6% (Ans) Again, We know, Eb= V – (Ia2 Ra) = 230-(79.08 × 0.3) = 206.28V Now, P= EbIa2= 206.28×79.08= 16312.6W H.P= = 21.8 H.P (Ans) | Given, V = 230V INL = 5A IFL= 80A Ra = 0.3Ω Rsh = 250Ω H.P= ? η =?
 | Given, V = 230V INL = 5A IFL= 80A Ra = 0.3Ω Rsh = 250Ω H.P= ? η =?

## Slide 15
AvMvgx K¬vm :
Aa¨vq-14 (wWwm ‡gvUi Pvjbv Ges MwZ wbqš¿b)
Pjgvb....

## Slide 16
Home Work:
1| wWwm †gvU‡ii jm wK ?
2| wWwm †gvU‡ii cvIqvi †÷R eY©bv Ki?
3| H.P ej‡Z wK eySvq?
4| 10 H.P ‡K Watt G cÖKvk Ki?
5| wWwm ‡gvU‡ii Av‡g©Pv‡i Drcbœ UK© m¤úwK©Z MvwYwZK mgm¨v|
Pjgvb....

## Slide 17
এই ভিডিও টি পুনরায় দেখতে দক্ষতাবাতায়ন
বা
www.skills.gov.bd ভিজিট করুন
Pjgvb....

## Slide 18
mevB‡K ab¨ev`....